## Slide 1: Label + Serial Number Change
Jacob Scott
jacob.scott@uwaterloo.ca
22-10-2021

## Slide 2: Overview
The Label Serial Number Project is intended to streamline the printing document/label process for construction by printing all documents/labels needed at the time when the shop order is scanned
The system will also handle serial numbers, and automatically update and reset the count when needed based on serial numbers given out, the week, and the year
The scanner is setup to press F9 when it in use, which will trigger the program to start
  A manual shop order print can be executed by pressing F9, typing the shop order out, then pressing Enter/Carriage Return
Follow the instructions on the command prompt window to print the desired documents/labels

## Slide 3: Example Label Outputs

## Slide 4: New Serial Number List

## Slide 5: New Quality Assurance Inspection Sheet

## Slide 6: How to Use the new Label Serial Number System
Key Programs:
  AutoHotkey
  Command prompt window
  Visual CUT
  Adobe Acrobat
  Microsoft Word
  Task Schedular
  SQL
The user generally only has to worry about the command prompt window, and it’s parameters

## Slide 7: AutoHotkey Running
Ensure AutoHotkey is running, otherwise the program will not boot up when scanned

## Slide 8: Post Printing Stage 1

## Slide 9: Post Printing Stage 2

## Slide 10: Advance Features
Booting the system yourself
  Hit F9, then the shop order, then Enter
Changing what’s being printed
  Go to Documents\labelSerialNumberProject\scanningProcess then edit the relevant database file (Labels, or Documents.txt) before confirming that your order number is correct on the start screen, but after booting the program
Printing a single label through Visual CUT
  Go to Visual CUT, and pick the label format you need to print to, then enter in the prompted relevant information, then go to the top left to print to the correct printer
Changing the Serial Number manually
  Go to Documents\labelSerialNumberProject\scanningProcess then edit SerialNumberCount.txt, the number is the next one that will be printed

## Slide 11: Trouble-shooting
If there is an issue the user is faced with that is unexpected:
AutoHotkey is not running
  There is a shortcut called initialize Scan on the desktop to boot it up
  Alternatively, you can navigate to the project folder*
SQL does not query
  Either the install has failed, or the connection is incorrect
    Navigate to the project folder* to updateSQL.bat and update the username and password
    Navigate to the install folder, and reinstall SQL Server, specifically SQLCMD.EXE
Serial Numbers isn’t updating
  If it is not updating per week/year, check that the Task Schedular task is still setup
Word/PDF Documents aren't printing
  Check to see if Word/Adobe is installed
  Navigate to the project folder* and checkout printWIP.bat or printWIPDocuments.bat
Crystal Reports…
  If the report is pulling the wrong information, check the database
  If the report isn’t pulling information, check the database
  If the report isn’t printing, check the error associated with Visual CUT
    The file printLabelsv2 may need to be adjusted if there is a new label type
*C:\Users\PXSPRNADM\Documents\labelSerialNumberProject\scanningProcess

## Slide 12: Reoccurring Programs
serialNumberYearlyUpdate.bat
Runs once a year on January 1st, 1AM
serialNumberWeeklyUpdate.bat
Runs once a week, on Sunday at 1AM
yearlyLogCleanup.exe – c++
Runs once a year, on January 1st 1AM.
Cleans bLog.txt of old barcodes, presumably not being used post SQL
Updates the SN to the next week, resets number
Updates the SN to the next year, resets week + number
Setup via Windows Task Scheduler

## Slide 13: Program Hierarchy SQL
initScan.exe (AHK)
updateSQL.bat
labelQuery.sql
documentQuery.sql
Labels.txt
Documents.txt
orderQuery.sql
Orders.txt

## Slide 14: Program Hierarchy Logic
logCheck.exe (C++)
bLog.txt
SNCountUp.bat
printWIP.bat
printSerialDocuments.bat
removeSQLqueries.bat
printWIPDocuments.bat
printLabelsv2.bat
SNCount.txt
print075.bat

## Slide 15: Windows Task Scheduler
initScan.exe runs on bootup of outgoing scanning computer
serialNumberWeeklyUpdate.bat runs once a week, on Sunday morning, on the outgoing scanning computer
serialNumberYearlyUpdate.bat runs at the beginning of the year on the outgoing scanning computer
yearlyLogCleanup.exe runs at the beginning of the year on the outgoing scanning computer

## Slide 16: Technical Debt
AutoHotkey needs to be installed on host computer
Need MinGW compiler on host computer
Git should be installed
MSSQL needs to be installed ideally though VSCode
Scanner needs to preamble with F9
User needs to type number of prints they want, defaulted order amount via SQL
Windows Task Scheduler will need to be setup on host computer, if it changes, the system will not work
  Bat files cant execute on network computers thus needs to be local
Percentage of barcodes removed every year is customizable
  Easily found in code of scannerUsageCheck.cpp
  And recompiled with g++
Add MinGW\bin to Path
Add Microsoft SQL Server\Client SDK\ODBC\170\Tools\Binn to Path
All files required to install are in \install

## Slide 17: Technical Debt Cont…
Location of data and relevant files is hyper dependent on code
System will be hard to move between computers
Report extract from ExactMAX is impossible to work with
Crystal reports wont intake a text file easily, serial number is being imported as a parameter from visual cut
  Tried ODBC text file
Ensure Microsoft Word is installed
Install SQL Server 2019 for SQLCMD.EXE
Ensure file paths are updated when downloading from GitHub
Don’t change any settings in Visual CUT for specific reports, as it can override the command line parameters
Task Schedular files are in \install
Set paper printer to default to duplex
https://github.com/pixustechnologies/labelSerialNumberProject

## Slide 18: Utilizing the System from BOM - Labels
Use a ? to include parameters to the label if applicable Do not exceed one line

## Slide 19: Utilizing the System from BOM - Documents
Use as much of the file path to the document, Then a ?, Then a unique string to identify the document Do not exceed one line

## Slide 20: GitHub account details
For future use

## Slide 21: GitHub account details
Username
pixustechnologies
Email
helpdesk@pixustechnologies.com
Password
Start with the highest shelf 2nd.