## Slide 1: Label + Serial Number Change
Jacob Scott
jacob.scott@uwaterloo.ca
13-09-2021

## Slide 2: Overview
The Label Serial Number Project is intended to streamline the printing document/label process by printing all documents/labels needed when the shop order is scanned
The system will also deal with serial numbers, and automatically update and reset the count when needed
The scanner is setup to press F9 when it in use, which will trigger the program to start
Follow the basic instructions on screen to print the desired documents

## Slide 3: Example Label Outputs

## Slide 4: New Serial Number List

## Slide 5: New Quality Assurance Inspection Sheet

## Slide 6: How to Use the new Label Serial Number System
Key Programs:
  AutoHotkey
  Command prompt window
  Visual CUT
  Adobe Acrobat
  Microsoft Word
  Task Schedular
  SQL
The user generally only has to worry about the command prompt window, and it’s parameters

## Slide 7: AutoHotkey Running
Ensure AutoHotkey is running, otherwise the program will not boot up when scanned

## Slide 8: Post Printing Stage 1

## Slide 9: Post Printing Stage 2

## Slide 10: Trouble-shooting
If there is an issue the user is faced with that is unexpected:
AutoHotkey is not running
  There is a shortcut called initialize Scan on the desktop to boot it up
  Alternatively, you can navigate to the project folder*
SQL does not query
  Either the install has failed, or the connection is incorrect
    Navigate to the project folder* to updateSQL.bat and update the username and password
    Navigate to the install folder, and reinstall SQL Server, specifically SQLCMD.EXE
Serial Numbers isn’t updating
  If it is not updating per week/year, check that the Task Schedular task is still setup
Word/PDF Documents aren't printing
  Check to see if Word/Adobe is installed
  Navigate to the project folder* and checkout printWIP.bat or printWIPDocuments.bat
Crystal Reports…
  If the report is pulling the wrong information, check the database
  If the report isn’t pulling information, check the database
  If the report isn’t printing, check the error associated with Visual CUT
    The file printLabelsv2 may need to be adjusted if there is a new label type
*C:\Users\PXSPRNADM\Documents\labelSerialNumberProject\scanningProcess

## Slide 11: Reoccurring Programs
serialNumberYearlyUpdate.bat
Runs once a year on January 1st, 1AM
serialNumberWeeklyUpdate.bat
Runs once a week, on Sunday at 1AM
yearlyLogCleanup.exe – c++
Runs once a year, on January 1st 1AM.
Cleans bLog.txt of old barcodes, presumably not being used post SQL
Updates the SN to the next week, resets number
Updates the SN to the next year, resets week + number
Setup via Windows Task Scheduler

## Slide 12: Program Hierarchy
initScan.exe (AHK)
logCheck.exe (C++)
bLog.txt
SNCountUp.bat
printWIP.bat
printQA.bat
updateSQL.bat
labelQuery.sql
documentQuery.sql
deleteSavedFiles.bat
printWIPDocuments.bat
removeSQLqueries.bat
printLabelsv2.bat
SNCount.txt
Labels.txt
Documents.txt

## Slide 13: Windows Task Scheduler
initScan.exe runs on bootup of outgoing scanning computer
serialNumberWeeklyUpdate.bat runs once a week, ideally Sunday morning, on the outgoing scanning computer
serialNumberYearlyUpdate.bat runs at the beginning of the year on the outgoing scanning computer
yearlyLogCleanup.exe runs at the beginning of the year on the outgoing scanning computer

## Slide 14: Technical Debt
AutoHotkey needs to be installed on host computer
Need MinGW compiler on host computer
Git should be installed
MSSQL needs to be installed ideally though VSCode
Scanner needs to preamble with F9
User needs to type number of prints they want, defaulted order amount via SQL
Windows Task Scheduler will need to be setup on host computer, if it changes, the system will not work
  Bat files cant execute on network computers thus needs to be local
Percentage of barcodes removed every year is customizable
  Easily found in code of scannerUsageCheck.cpp
  And recompiled
Install SQL Server 2019 for SQLCMD.EXE
Add MinGW\bin to Path
Add Microsoft SQL Server\Client SDK\ODBC\170\Tools\Binn to Path

## Slide 15: Technical Debt Cont…
Location of data and relevant files is hyper dependent on code
System will be hard to move between computers
Report extract is impossible to work with
Crystal reports wont intake a text file easily, serial number is being imported as a parameter from visual cut
  Tried ODBC text file
Ensure Adobe Acrobat and Microsoft Word is installed
Adobe Acrobat can’t print silently
Ensure file paths are updated when downloading from GitHub
Set paper printer to default to duplex
https://github.com/pixustechnologies/labelSerialNumberProject

## Slide 16: GitHub account details
For future use

## Slide 17: GitHub account details
Username
pixustechnologies
Email
helpdesk@pixustechnologies.com
Password
Start with the highest shelf 2nd.